07.01.07

Audicator Programming Instructions

(Double click on these symbols to hear sounds)

Your Audicator is supplied with default settings that we feel are most appropriate for the majority of users. However, if any aspect of the program settings are not to your liking it is very easy to change by using the power lead supplied and following these simple instructions:

1/	Connect (constant) power to either indicator wire (blue or yellow) - unit will enter programming mode and emit a regular 4 note tune.

2/	During a silent phase in this sequence, enter the program variable you wish to adjust by pulsing the vehicle brake the appropriate number of times - unit will ‘beep-back’ the same number to you.

3/	Pulse the brake the appropriate number of times to set that variable to your desired level; the unit will then ‘beep-back’ the same number to you.  Note: this operation must be carried out within 10 seconds of operation 2 or the unit will revert to programming mode

4/	your variable is now set to your requirements and the unit will return to programming mode  ready for modification of any other variable or simply disconnect power lead to return to normal use mode.

| Variable Number | Description | Notes and default setting |
| --- | --- | --- |
| 1 | Number of silent indicator flashes | Number of flashes before unit is audible – default setting is 10 flashes |
| 2 | Number of volume ramps (0 – 7) | Number of volume ramp levels before maximum - default setting is 3 |
| 3 | Number of audible beeps per volume ramp-up | Number of flashes in each volume ramp level before changing to next level – default setting is 3 |
| 4 | Alternative sounds for flasher audible | Unit will scroll around all available sounds operate brake after your desired sound is heard |
| 5 | Number of audible Hazard flashes | When hazards activated on vehicle, number of flashes before silent – default setting is 50 |
| 6 | Alternative sounds for Hazard audible | Unit will scroll around all available sounds operate brake after your desired sound is heard |
| 7 | Initial beep on/off | Initial beep when indicators activated – select 1 for beep or 2 for no beep – default setting is on |
| 8 | Reset factory default settings | Select this variable to restore all settings to factory default. |

Important – ensure at least a 5 second delay after changing from programming mode to normal operation, in order for your program changes to take effect.